## Slide 1
L4: Device & Block Layers
Chun-Feng Wu (吳俊峯)
Assistant Professor, National Yang Ming Chiao Tung University
cfwu417@cs.nycu.edu.tw
https://cfwu417.github.io

## Slide 2: Recall: Multi-Level Cells
Is it possible to let a cell represent more than one bit?
  Ans: A cell can represent two bits, if there are 4 verifiable voltage states in the cell
Single-Level Cell (SLC): One-bit per cell
Multi-Level Cell (MLC): Multiple-bits per cell, 2#bits voltage levels
P-substrate
n-source
n-drain
Control gate
Dielectric
2-bits MLC
11  No Electron
10  1/3 Electrons
01  2/3 Electrons
00  Full Electrons
Illustration of 2-bits MLC
Illustration of 3-bits MLC (or TLC)
Ref: https://www.kioxia.com/en-jp/rd/technology/multi-level-cell.html
Why distributions?

## Slide 3: Recall: SSD’s Architecture
Flash Translation Layer:
  Sequential Write Constraint  Sol: Address Remapping (Logical Block Address to Physical Block Address) + Garbage Collection
  Limited Lifetime  Sol: Wear Leveling
Memory Technology Device (MTD): Interact (read/program) with NAND Flash chips.
SSD
NAND Flash Chips
Controller
Flash Translation Layer (FTL)
NAND Flash Chips
NAND Flash Chips
NAND Flash Chips
NAND Flash Chips
NAND Flash Chips
Device Driver
Address Translator
Garbage Collector
Wear Leveler
DRAM
Data Buffer
Translation Table
Memory Technology Device (MTD)
1010111100111110000101010
NAND Flash Page
……
NAND Flash Block 1
…
NAND Flash Block 2
NAND Flash Page (Latest)
1110011000110110110101001
Read Modify
Write
LBA 500
PBA 800
LBA 500  PBA 1201
Update the Mapping
Mark as invalid

## Slide 4: Recall: Interaction with the Peripherals
How CPU accesses peripherals
  Port-Mapped I/O (Isolated I/O): CPU accesses peripherals by IN/OUT instructions where the I/O address space is separated from the memory address space.
  Memory Mapped I/O: CPU accesses peripherals by load/store instructions where the I/O address space is shared with the memory address space.
Direct Memory Access (DMA): Transfer data directly between memory and I/O devices without CPU’s interventions.
CPU
CPU
load/store
load/store
I/O Addr.
Memory Addr.
I/O Device
0x0000
0xFFFF
I/O Addr.
Memory Addr.
I/O Device
0x0000
0xFFFF
in/out
I/O Ports
load/store
Memory Address
Port-Mapped I/O
Memory-Mapped I/O
CPU
DMA
Memory
I/O Device
DMA Controller

## Slide 5
Device Driver
Process
Virtual File System
Page Cache
Mapping Layer (FS Specific)
User
Kernel
sys_read()
sys_write()
Devices
(e.g., HDD, SSD)
Block Device Driver
Block I/O Layer

## Slide 6: A Split View of the Kernel I/O Stacks
Block Devices: Addressable in device-specified chunks called blocks and generally support seeking, the random access of data.
  Mounted as a file system
  Suited for handling data blocks with a fixed number of bytes.
Character Device: Providing access to data only as a stream, generally of characters (bytes)
  Suited when the volumes of data transferred are low.
Keyboard
Mouse
SAS Devices
Applications
USB Devices
PCIe Bus
Keyboard Device Driver
Mouse Device Driver
SAS Device Driver
USB Device Driver
PCIe Bus Device Driver
Hardware
Kernel
Kernel I/O Subsystem
Keyboard Device Controller
Mouse
Device Controller
SAS
Device Controller
USB
Device Controller
PCIe Bus
Device Controller
(Block)
(Block)
(Character)
(Character)
(Character)

## Slide 7: More About Device Driver
70% of Linux kernel code is device driver
Compositions of device driver (Linux 2.6):
  52% Char device drivers
  16% Block device drivers
  27% Network device drivers
An example of network device driver
[1] L. Ryzhyk, P. Chubb, I. Kuz, and G. Heiser. Dingo: Taming device drivers. In Eurosys, 2009.
Pack/Unpack USB packets
Export network interface
Linux Network Stack
Notes: The driver implements the Ethernet family protocol that exports the network interface functionality to the OS network stack.
Since the device in question is connected to the USB bus, it cannot be accessed by the driver directly. Instead, device protocol messages must be encapsulated in- side USB data packets submitted to the USB bus driver via the USB family protocol. Such driver stacking is common in operating system I/O frameworks and reflects the structure of the underlying I/O bus hierarchy.

## Slide 8: The Role of the Device Driver
Device Driver: A computer program that operates or controls a particular type of device that is attached to a computer. (Hide the details of how device works)
Device (Special) File: Used to interact with drivers for accessing expansion devices. Easier for users to identify corresponding devices.
Kernel modules (e.g., device drivers) are a piece of code, that can be loaded and unloaded from kernel on demand.
Ref: Mauerer, Wolfgang. Professional Linux kernel architecture. John Wiley & Sons, 2010

## Slide 9: How to Build a Device Driver
Module_init: Kernel runs a function when the module is loaded.
  Format: int my_init(void);
  Output: Return 0 if it is successful
  Purposes: Initialize hardware, allocate data structures.
Module_exit: Kernel runs a function when the module is removed.
  Purposes: Free resources, shutdown and reset hardware.
MODULE_LICENSE: Specifies the copyright license for this file.
Linux Kernel Development, 3rd Edition

## Slide 10: How to Build a Device Driver (Count.)
Source Tree: (1) Store driver code (e.g., c files) in the correlated directory (e.g., drivers/block or drivers/char). (2) Modify the Makefile in the directory (Please refer to P.341 in the textbook, Linux Kernel Development.
Build Externally: Maintain and build our module outside the kernel source tree. Create a Makefile by adding two commands
  obj-m := hello_world.o
  make –C /lib/modules/$(shell uname –r)/build M=$(PWD) modules
Compiles hello_world.c into hello_world.ko
Go to the directory and read the Makefile
Go back to the prior directory and read the Makefile

## Slide 11: Kernel Programming
How to access the ``current’’ process: Kernel code can access the global item current, which has a pointer points to struct task_struct.
  Why it works: most actions run by the kernel are done on behalf of a specific process.
  Ex: printk(KERN_INFO "The process is \"%s\" (pid %i)\n",current->comm, current->pid);
Process A
User Mode
Process A
Kernel Mode
User Program
Process Data
User Mode
System Call!!
Kernel Module
Kernel Mode
Kernel Address Space (Virtual)
User Address Space (Virtual)
Main Memory
CPU

## Slide 12: Kernel Programming (Count.)
How to access the current process: Kernel code can access the global item current, which has a pointer points to struct task_struct.
  Why it works: most actions run by the kernel are done on behalf of a specific process.
  Ex: printk(KERN_INFO "The process is \"%s\" (pid %i)\n",current->comm, current->pid);
Cautions for kernel programming:
  Super small stack: With using virtual memory, applications have large stack area virtual memory, the kernel instead has a very small stack (Only 1~2 pages).
  Kernel function with _ _: Usually low-level components. Should be used with caution.
  Do not use floating points: Floating point support is very expensive in the kernel and should be avoided.
Why expensive: Shall save floating-point registers while switching from user to kernel mode (hundred of cycles)
Notes: https://stackoverflow.com/questions/13886338/use-of-floating-point-in-the-linux-kernel

## Slide 13
Block I/O Layer
Process
Virtual File System
Page Cache
Mapping Layer (FS Specific)
User
Kernel
sys_read()
sys_write()
Devices
(e.g., HDD, SSD)
Block Device Driver
Block I/O Layer

## Slide 14: Buffers and Buffer Heads
Sector
Sector: The smallest addressable unit of the storage device. (e.g., 512 B)
Block: The smallest addressable unit of the file system. (e.g., 512 B)
  Size(Page)>=Size(Block) >= Size(Sector)
Buffer: The object which represents a block in memory.
Buffer Head: A descriptor (i.e., struct buffer_head) for each buffer. (e.g., the buffer is from which block device and from which specific block)
b_page points to the corresponding page for storing the block.
b_data points to the starting point of the block
b_bdev points to the corresponding block device
b_size indicates the size of the block
b_state specifies the state of the buffer. (e.g., dirty, lock)
Memory Page (4KB)
Sector
Storage Device
Block
Block
Buffer

## Slide 15: Challenges of Buffer Heads
Buffer heads play the role of buffer-to-block mapping.
Challenge 1: A large and bulky data structure. A block is smaller than a page, and each buffer is described by a bulky buffer head, thus inefficient.
  Sol (2.6 kernel): kernel works directly with pages and address spaces instead of blocks.
Challenge 2: kernel shall break up large block I/O operations into multiple needless buffer_head structures (e.g., each buffer_head represent 512 B).
  Sol (2.5 kernel): A new, flexible, and lightweight container for block I/O operations. (bio)

## Slide 16: BIO Structure
Segment
Bio: A block I/O operation. It can handle a list of non-contiguous segments. (Blocks belonging to an operation need not be contiguous)
Segment: A chunk of a buffer that is contiguous in memory.
Segment
<page, offset, len>
Page Frame
Current processing segment (Help to keep track of current progress)
One block I/O operation (*bi_next can point to next operation)
Start of the vec_list belonging to the I/O operation
Ref: https://www.byteisland.com/linux-%E9%80%9A%E7%94%A8%E5%9D%97%E5%B1%82-bio-%E8%AF%A6%E8%A7%A3/
Notes: Even though bio has replaced buffer_head for most file data I/O, buffer_head is still used in many filesystems (like ext4) to read and write metadata (e.g., superblocks, group descriptors, bitmaps, inodes).